## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
PROBLEM STATEMENT METADATA:
Problem Statement ID — 26050
Problem Statement Title — High Altitude Performance Optimization and Robust Design of Anti-Drone System
Project Solution Title — HIGH-ALTITUDE RUGGEDIZED ANTI-DRONE DETECTION & PRECISION TRACKING SYSTEM WITH AI-BASED ENVIRONMENTAL COMPENSATION
Theme — Robotics and Drones / Defence & Security
PS Category — Software / Hardware Integration (Hybrid)
Team ID — SIH2026-PS26050-TEAM
Team Name — HAADS SIH 26050

## Slide 2: IDEA TITLE
PROBLEM (HIGH-ALTITUDE OPERATIONAL STRESS):
• Extreme cold (-30°C) affects motor pulse response, lubricant viscosity, and mechanical cable stiffness.
• Low atmospheric pressure (500 hPa) changes air density and dynamic aerodynamic behaviour.
• High wind gusts (60 km/h) cause severe aerodynamic drag (2.55 N) and target-pointing drift.
• Mountain glare and atmospheric haze reduce visual sensor reliability.
• Uncompensated environmental variation causes tracking instability and target acquisition loss.
PROPOSED SOLUTION (INTEGRATED HARDWARE + AI EDGE VISION):
• Real-time YOLO26n-based visual object detection (sub-40ms edge inference).
• SORT-based persistent target tracking maintaining track IDs with center locking (320, 240).
• BME280 environmental monitoring (Temperature + Atmospheric Pressure + Humidity).
• MPU6050 6-axis IMU for tilt, motion, and structural vibration monitoring.
• Anemometer wind-speed sensor for real-time aerodynamic drag compensation.
• Environment-aware compensation engine scaling servo pulse signals (Stiffness factor x1.5).
• ESP32 DevKit V1 telemetry communication through HiveMQ MQTT broker.
• 2-axis Pan-Tilt servo mechanism for physical target-centred tracking.
• Piezo buzzer local alert indication (GPIO 25 @ 2000Hz tone).
INNOVATION & INTEGRATED CHAIN:
Environment sensing + AI edge detection + persistent tracking + dynamic compensation + pan-tilt servo control in one unified system.
📌 INTEGRATED FLOW: SENSORS (BME280/MPU6050/Wind) ➔ AI DETECTION (YOLO26n) ➔ TARGET TRACKING (SORT) ➔ COMPENSATION ENGINE ➔ PAN-TILT SERVO CONTROL ➔ TARGET LOCK
HAADS SIH 26050

## Slide 3: TECHNICAL APPROACH
1. REAL PHYSICAL HARDWARE COMPONENTS (PROTOTYPE BOM):
• ESP32 DevKit V1: Main 32-bit dual-core microcontroller, sensor acquisition, PWM servo control, MQTT Wi-Fi telemetry.
• BME280 Sensor Module: Ingests ambient Temperature, Atmospheric Pressure, and Relative Humidity.
• MPU6050 IMU Module: Measures 3-axis acceleration, tilt/orientation angles, and structural vibration.
• Anemometer / Wind Speed Sensor: Real wind-speed measurement used for aerodynamic drag force compensation.
• SG90 / MG90S Servo Motors: 2 precision servo motors (One for PAN azimuth, One for TILT elevation).
• 2-Axis Pan-Tilt Camera Bracket: Mechanical gimbal mounting structure holding and moving the camera payload.
• USB Webcam: Real camera visual input for physical target detection and tracking.
• Piezo Buzzer: Local audible alert output indicating target lock and system events (GPIO 25).
• 10kΩ Potentiometers: Manual testing and threshold calibration inputs.
• 5V Regulated Power Supply & Power Bus: Provides clean DC power for servos and microcontroller peripherals.
• Breadboard & Jumper Wires: Circuit wiring and inter-module signal connections.
2. COMPUTING & AI EDGE PLATFORM (LAPTOP / SYSTEM):
• Laptop / Computer: Runs Python 3.12, OpenCV 4.x, YOLO26n Edge AI model, SORT Tracker, and Streamlit Dashboard.
3. COMMUNICATION ARCHITECTURE:
• ESP32 DevKit ──[Wi-Fi / HiveMQ MQTT Broker]──> Python Hardware Interface ──> Streamlit Dashboard
4. SIMULATION VALIDATION LINK (WOKWI):
• WOKWI SIMULATION: Virtual ESP32 platform used for hardware-in-the-loop validation before physical wiring.
5. END-TO-END SYSTEM DATA FLOWS:
• MAIN VISION FLOW: USB WEBCAM ➔ OpenCV ➔ YOLO26n ➔ SORT TRACKER ➔ CENTROID LOCK ➔ COMPENSATION ➔ ESP32 ➔ PAN/TILT SERVOS
• ENVIRONMENT FLOW: BME280 + MPU6050 + ANEMOMETER ➔ ESP32 ➔ MQTT TELEMETRY ➔ LAPTOP ➔ DYNAMIC COMPENSATION ENGINE
HAADS SIH 26050

## Slide 4: FEASIBILITY AND VIABILITY
TECHNICAL FEASIBILITY:
• ESP32 DevKit provides highly reliable, low-cost embedded control for sensor sampling and servo PWM generation.
• BME280, MPU6050, and anemometer supply accurate environmental telemetry for dynamic software compensation.
• 2-axis servo pan-tilt mechanism enables clear physical target tracking demonstration.
• Laptop CPU/GPU handles real-time YOLO26n Edge AI vision and SORT tracking during the prototype phase.
• Wokwi simulation enables safe virtual hardware testing before physical assembly.
• Modular system design supports seamless transition to standalone embedded edge hardware (e.g. Jetson Orin).
OPERATIONAL CHALLENGES:
• Extreme cold (-30°C) increasing cable resistance, lubricant viscosity, and motor torque demand.
• Low atmospheric pressure (500 hPa) altering air density and thermal dissipation efficiency.
• High wind disturbance (60 km/h) inducing aerodynamic drag force (2.55 N) and pointing drift.
• Mechanical vibration and chatter caused by high-altitude winds.
• Sensor drift and visual glare under intense high-altitude sunlight.
• Servo positioning backlash and potential MQTT communication network latency.
MITIGATION STRATEGIES:
• Temperature-aware pulse compensation multiplying servo drive gain (Stiffness factor x1.5).
• Wind-speed based aerodynamic drag calculation and automatic pan/tilt angular offset correction.
• IMU-based vibration monitoring and adaptive stabilization filtering.
• Sensor validation and noise rejection algorithms.
• SORT persistent object tracking preserving target Track IDs through momentary camera glare drops.
• Servo position feedback control and MQTT heartbeat liveness monitoring.
• Truthful 9-subsystem health monitor providing complete operator visibility.
HAADS SIH 26050

## Slide 5: IMPACT AND BENEFITS
TARGET APPLICATIONS & USER DOMAINS:
• High-altitude security installations and remote defense outposts (Himalayan border sectors).
• Mountainous border surveillance and perimeter monitoring corridors.
• Critical national infrastructure protection (power plants, communication relays, airbases).
• Defense R&D laboratories and prototyping testbeds.
• Non-kinetic anti-drone detection, tracking, and authorized response research.
SYSTEM BENEFITS:
• Environment-aware tracking resilient against severe atmospheric and thermal stress.
• Improved pointing stability and reduced target acquisition loss under strong wind gusts.
• Real-time environmental monitoring (Temperature, Pressure, Wind Speed, Vibration).
• Real-time operator visibility into complete system health via 9-subsystem health matrix.
• Modular hardware architecture allowing straightforward component upgrades and maintenance.
• Low-cost simulation-first development model combining Wokwi ESP32 and open-source AI tools.
• Scalable edge-AI architecture designed for easy future transition to rugged field deployment.
SCALABILITY ROADMAP:
• CURRENT PROTOTYPE: Laptop + USB Webcam + Wokwi ESP32 Simulation & MQTT Telemetry Link.
• PHYSICAL PROTOTYPE: ESP32 + BME280 + MPU6050 + Anemometer + USB Webcam + 2-Axis Servos + Buzzer + 5V Supply.
• FUTURE FIELD DEPLOYMENT: Embedded Edge AI (Jetson Orin) + Ruggedized IP67 Enclosure + High-Altitude Field Operations.
HAADS SIH 26050

## Slide 6: RESEARCH AND REFERENCES
GENUINE TECHNICAL & RESEARCH REFERENCES:
• [1] YOLO / Ultralytics Documentation: Real-time object detection models and edge vision deployment benchmarks.
• [2] SORT Tracking Algorithm (Bewley et al.): Simple Online and Realtime Tracking for persistent target centroid locking.
• [3] ESP32 Microcontroller Documentation (Espressif Systems): ESP32 dual-core architecture, PWM, and Wi-Fi stack.
• [4] Bosch BME280 Sensor Datasheet: Environmental sensing principles for barometric pressure, temperature & humidity.
• [5] MPU6050 IMU Datasheet (InvenSense): 6-axis motion tracking, accelerometer, and gyroscope processing.
• [6] Anemometer Measurement Principles: Principles of wind-speed measurement and aerodynamic drag calculation.
• [7] Wokwi Simulator Documentation: Virtual microcontroller hardware simulation platform for ESP32 and IoT modules.
• [8] MQTT Protocol Specification (OASIS Standard): Lightweight publish/subscribe messaging transport for IoT telemetry.
• [9] MIL-STD-810H Military Standard: Environmental engineering considerations and laboratory tests for high altitude & extreme cold.
HAADS SIH 26050